## Slide 2: Learning objectives
In this lesson students will learn to:
  Draw a diagram of the inside of a computer and label each hardware component
  Explain the role of components of the CPU (the CU, ALU and registers)
  Describe the role of the clock and explain how the speed of the clock impacts on performance.
For more details on this topic and additional student activities see Topic 3 of the student book.
Notes: Specification content: 3.1.1

## Slide 3: Recap
Instructions and data are stored in the memory (RAM).
Instructions are fetched one at a time into the processor.
The instructions are decoded by the control unit.
The instructions are executed, sometimes using the arithmetic logic unit

## Slide 4: Central Processing Unit
The CPU is the 'brain of the computer’.
It is the hardware component responsible for all the processing that the computer carries out.
Its job is to process data. By processing, we mean things such as searching, sorting, calculating and decision making.
Whenever you are on working on your computer, it is the CPU that is at the centre of everything.
Notes: The giving of human qualities to a machine, called ‘anthropomorphism’, is something you need to be very careful about doing in the context of computers. In this example, the ‘brain’ means the ‘centre of processing’. It does not mean that a machine can think or reason. Ensure that other qualities of the human brain are not attributed to machines by making this difference clear.

## Slide 5: Control unit
The control unit receives signals from other parts of the computer system and sends signals to them.
It is responsible for handling hardware interrupts (e.g. inputs from a mouse, keyboard, network, etc.).
It is responsible for fetching, decoding, and executing instructions.
It is the powerhouse of the CPU – it has the most responsibility.
Notes: The CU is much like the conductor in an orchestra. As in an orchestra, there are lots of instruments, which all play a part when called upon, but only when the conductor dictates.

## Slide 6: Arithmetic logic unit
The Arithmetic Logic Unit (ALU) performs actual operations on data.
  Arithmetic: + / = *
  Logic: AND, OR, NOT, etc.
It is able to compare numbers against 0.
It can test if two numbers are equal.
It uses logic gates in combination to perform operations.
Notes: Students may have already been doing arithmetic and Boolean logic (AND, OR, NOT) in their programs. Physical logic gates implement the truth tables found in Topic 1.
O = opcode to perform; S = status after operation; A, B = operands (data); X = result. Students should be familiar with the symbol, but not the arguments.

## Slide 7: Registers
Also known as immediate access storage.
Registers are a type of memory that is extremely fast, much faster than RAM.
Each type of processor has different registers that are designed to hold different information.
Most processors have:
  an instruction register: holds instruction currently being executed by the CPU.
  an accumulator: holds the accumulated result of operations carried out by the ALU.
  a program counter: holds the memory address of the next instruction to be executed.
Notes: Student Activity 1

## Slide 8: Clock
A clock chip determines the speed of the CPU.
This chip uses a vibrating crystal that maintains a constant rate of vibration.
The speed of the clock is measured in Hertz (Hz), which is the amount of cycles per second.
A clock speed of 500Hz means 500 cycles per second.
Current computers have clock speeds of 3GHz, which means 3-billion cycles per second.
Each ‘tick’ means that one part of the fetch-decode-execute cycle can be carried out.
Notes: Note: clock ticks ≠ instructions completed. They are not directly related due to processing overheads.

## Slide 9: Pipelining
Each instruction that is carried out has several stages (fetch-decode-execute).
Each component of the CPU has a different job to do in this cycle.
Sometimes, one component has nothing to do whilst it is waiting for the component before it in the sequence to complete its task.
This increases the overall processing time needed.
Pipelining is a method of keeping all the components busy so as to improve overall CPU performance.

## Slide 10: Pipelining
Pipelining attempts to keep every component of the CPU busy at all times.
Instructions flow through the CPU in stages.
This means that an instruction can be completed every clock cycle. This increases CPU throughput allowing overall performance to be optimised.
A CPU is called ‘fully pipelined’ if an instruction can be fetched every clock cycle.
Notes: By staggering the operations, one instruction can be fetched, one can be decoded, and one can be executed, in parallel on one clock cycle. Students do not need to know about pipelining so slides 9 and 10 can be omitted.
Student Activity 2

## Slide 11: Wrap up: you have learned how to…
Draw a diagram of the inside of a computer and label each hardware component.
  CPU contains the CU, ALU and registers.
  The other components a computer needs include: input and output devices, RAM, motherboard, and power supply unit.
Explain the role of components of the CPU
  The CU decodes instructions and oversees their execution
  The ALU carries out arithmetic and logic operations on data
  Registers provide temporary storage
Describe the role of the clock and explain how the speed of the clock impacts on performance.
  The clock synchronises the actions of other components
  The faster the clock speed, the more instructions can be carried out per second.